## Slide 1: CMPS 3130/6130 Computational Geometry Spring 2017
Motion Planning
Carola Wenk

## Slide 2: Robot motion planning
Given: A floor plan (2d polygonal region with obstacles), and a robot (2D simple polygon)
Task: Find a collision-free path from start to end
Robot R is a simple polygon; R=R(0,0)
Let R(x,y) = R+ R translated by
Add rotations: R(x,y,)

## Slide 3: Configuration space
# parameters = degrees of freedom (DOF)
Parameter space = “Configuration space” C:
  2D translations: configuration space is C = R2
  2D translations and rotations: configuration space is C = R2 x [0,2)
Obstacle P. Its corresponding C-obstacle P’={C | R(
Free space: Placements (= subset of configuration space) where robot does not intersect any obstacle.
P’

## Slide 4: Translating a point robot
Work space = configuration space
Compute trapezoidal map of disjoint polygonal obstacles in O(n log n) expected time (where n = total # edges), including point location data structure
Construct road map in trapezoidal map:
  One vertex on each vertical edge
  One vertex in center of each trapezoid
  Edges between center-vertex and edge-vertex of same trapezoid
  O(n) time and space

## Slide 5: Translating a point robot
Work space = configuration space
Compute trapezoidal map of disjoint polygonal obstacles in O(n log n) expected time (where n = total # edges), including point location data structure
Construct road map in trapezoidal map:
  One vertex on each vertical edge
  One vertex in center of each trapezoid
  Edges between center-vertex and edge-vertex of same trapezoid
  O(n) time and space
Compute path:
  Locate trapezoids containing start and end
  Traverse this road map using DFS or BFS to find path from start to end
Theorem: One can preprocess a set of obstacles (with n = total # edges) in O(n log n) expected time, such that for any (start/end) query a collision-free path can be computed in O(n) time.

## Slide 6: Minkowski sums
P’

## Slide 7: Extreme points

## Slide 8: Configuration space with translations and rotations

## Slide 9: Shortest path for robot
Pull rubber band tight:

## Slide 10: Visibility graph